## Slide 1: HV connection for a Common GEM foil design
Aiwu Zhang
2015-03-09

## Slide 2
The foil is divided to sectors on the top,
while it is not segmented on the bottom.
550 mm
~946 mm
30 degrees

## Slide 3
Center line
Vias are used. red color stuff on top foil, blue color stuff on bottom foil.
-> Explain on HV connection:
2. 12 FIT HV pads all on top foil. (6 for top HV and 6 for bottom HV). We bring these pads, using spring pins, to the drift board to make HV connection. For a triple-GEM, we cut away 8 of the pads on each foil to allow spring pins go through the foil.
3. For FIT, we use 10M SMD resistors for each sector for protection. After the resistors, we have a common HV line goes to the 6 FIT HV pads. We also have a short common HV line on the bottom, goes to the 6 FIT HV pads through vias.
4. For UVa, their protective resistors are not on the foil, and they want to be able to test each sector once the chamber is closed. So individual HV pads are arranged for UVa, those pads are connected to each sector through the vias.
A global view at the wide end.
12 FIT HV pads
UVa HV pads
FIT protective resistors

## Slide 4
-> Explain on mechanically assembling a chamber:
6. The gray pads, with a 2 cm pitch, are mechanical holes on the foil. UVa can use them to close a chamber; FIT can use them to make a GEM stack for stretching.
7. For FIT, we need to have square holes in the foil, to allow us put nuts in for stretching. The square holes must be siting in the same row of those mechanical holes. (note that FIT HV pads are also in the same row.)
A global view at the wide end.
Center line
Mechanical holes
Square mechanical holes for FIT stretching

## Slide 5
The left part
Note that we have 4 horizontal sectors at lower end, the left 4 resistors are connected to those sectors.
Vias needed
(connect red trace to blue trace)

## Slide 6
~6.1mm
20mm
3mm
3mm
5.8mm
9.5mm
3mm
Dimensions. Need to optimize, especially along the R direction.
All trace width: 0.2mm
Copper edge of a foil
1.8mm

## Slide 7
2.5mm
Dimensions. Need to optimize, especially along the R direction.
Just pay a little attention to that corner (will be the same at the right side of foil)
15mm

## Slide 8
ref.: High Voltage Engineering - J R LUCAS, 2001 (Chapter 1)
Breakdown voltages for Ar and CO2:
Ar: 0.9 torr cm = 0.9*0.001358*10 atm mm
=0.01222 atm mm
at 1 atm, it is 137/0.01222 = ~11211 V/mm
-> breakdown happens at ~1100 V for a 0.1mm gap.
CO2: 420/(0.51*0.001358*10)=60642V/mm
-> breakdown happens at 6064V for a 0.1mm gap.

## Slide 9
UVa HV pads
FIT HV pads
(for top)
FIT HV pads
(for bottom)
Holes for
assembling
UVa HV pads (for bottom). Can be on top and connects through a via
Square holes for
FIT for stretching
FIT resistor
Common HV line
A via
Backup